4DOS DOCUMENTATION
               FOR DISKLESS WORKSTATION SETUP ON NETWARE 386

                          > > > CONFIG.SYS < < <

BREAK=ON
DEVICE=HIMEM.SYS /MACHINE:AT
DEVICE=EMM386.EXE 384 /frame=e000 /ram=c600-d7ff /ram=dc00-dfff
DEVICEHIGH=ANSI.SYS
DEVICEHIGH=BURNDEV.SYS 21600 H+ F5

SHELL=4DOS.COM @\4DOS.INI /P /F
BUFFERS=40
FILES=20
DOS=HIGH,UMB

                           > > > 4DOS.INI < < <

;                              4DOS.INI
;               4DOS Initial setup file used in startup

4StartPath=\
AutoexecPath=\
HelpPath=\
;LogName=F:\LOGIN\DW014DOS.LOG
Swapping=EMS,XMS
SwapReopen=NO ;YES if swapping 4DOS to Netware drive, NO for other drives.
;  //WARNING -- If set to YES, swap location -MUST- be a network drive or
;  will crash workstation if swap invoked.  (See "Swapping" parm. above).

EnvFree=512 ;Amount of environment to make free for 2ndary shells
UMBLoad=YES
Ansi=YES
BatchEcho=YES ;Echo batch commands unless ECHO OFF is received
CursorIns=40
CommandSep=^
HistMin=3
HistWinColor=BLACK on GREEN border WHITE
ColorDir=HIDDEN:red; DIRS:green
UpperCase=NO
NetwareNames=YES ;Must be set to YES if PC is on Novell network

                         > > > AUTOEXEC.BAT < < <

REM AUTOEXEC.BAT
REM Diskless Workstations, 4DOS

IF NOT "%_4VER%" == "" AUTOEXEC.BTM

                         > > > AUTOEXEC.BTM < < <

REM AUTOEXEC.BTM
REM 4DOS AUTOEXEC for Diskless Workstation

MODE CO80
PATH F:\LOGIN
SET COMSPEC=F:\LOGIN\4DOS.COM

REM Define system configuration for network (used in system login script):
SET PC_TYPE=CLONE
SET PC_CPU=386
SET PC_MON=VGA
SET PC_DFTDRV=F:
SET PC_DFTPRT=

ECHO OFF
PROMPT $P$G
ECHO.

ECHO Network, memory resident programs and 4DOS will be loaded next. 
WAIT
ECHO.
LOADHIGH IPX
EMSNETX

F:
REM 4DOS vars/commands
IF "%_4VER%" == "" GOTO NO4DOS
SET COMSPEC=F:\PUBLIC\4DOS\4DOS.COM
SET TEMP4DOS=
SETDOS /I-HELP /I-LIST
LOADHIGH KSTACK
ALIAS /R ALIAS.LST
LOG OFF

:NO4DOS
SET PCTV=/COLOR
SET LIST=
SET TEMP=

LA +AA /C >NUL

IF "%_4VER%" == "" GOTO :EXIT
  ECHO.
ECHO Available Base memory: %@DOSMEM[K]k
ECHO Available Expanded memory (EMS): %@EMS[K]k
ECHO Available Extended memory (XMS): %@XMS[K]k

:EXIT
VER

 ----------------------------------------------------------------------------

                      SAMPLE BOOT IMAGE CREATION LOG
             WITH DIR LISTS FOR A: (BOOT IMAGE DISKETTE) & F:\LOGIN

[PROGCARE #1-SUPERVISOR]
+A:\>dir

 Volume in drive A is DISKLESS WS    Serial number is 2C24:5810
 Directory of  a:\*.*

burndev.sys      2595   4-13-89  12:16
wait.com          128   6-01-90   0:24
ansi.sys         9029   4-09-91   5:00
command.com     47845   4-09-91   5:00
netx.com        51201   7-31-91  10:47
emsnetx.exe     63838   7-31-91  10:49
emm386.exe     110174   3-10-92   3:10
himem.sys       13824   3-10-92   3:10
4dos.com       110082   6-08-92   4:01
4dos.ico          766   6-08-92   4:01
4dos.pif          545   6-08-92   4:01
4dosm.ico         766   6-08-92   4:01
shell.cfg         133   9-11-92  21:57
ipx.com         29213   9-15-92  19:59
4dos.ini          769   9-24-92  20:30
autoexec.btm      884   9-24-92  21:10
config.sys        234   9-24-92  21:13
autoexec.bat       91   9-24-92  21:14
     442,117 bytes in 18 file(s)           448,000 bytes allocated
     694,272 bytes free

[PROGCARE #1-SUPERVISOR]
+F:\LOGIN>dir

 Volume in drive F is SYS            Serial number is 7153:7CD9
 Directory of  f:\login\*.*

.            <DIR>
..           <DIR>
LOCAL        <DIR>      5-21-92   0:25
console.com       103   8-25-87   7:57
reboot.com        512   6-04-90   0:17
rprinter.hlp      117   8-09-90  22:40
token.rpl       13085  11-01-90  10:21
nlogin.exe      52944  11-02-90  16:02
slist.exe       22437   1-24-91   7:10
rprinter.exe    92378   2-06-91   7:39
loginnw.exe    108619   6-04-91  16:09
use.exe          6240   7-07-91  14:31 Add dynamically to PATH
exit&out.bat      627   2-24-92  16:20
4dos.com       110082   6-08-92   4:01
4dos.ico          766   6-08-92   4:01
4dos.pif          545   6-08-92   4:01
4dosm.ico         766   6-08-92   4:01
kstack.com        555   6-08-92   4:01
gaentry.bat       211   6-18-92  22:02
gm.bat             31   7-20-92  22:13
sup.bat           362   8-05-92  22:58
logout.bat       1288   8-07-92  21:47
menu.bat          361   8-18-92  18:51
loginmm.bat       640   8-18-92  18:52
entry.bat         204   8-29-92  10:15
ke.bat            355   9-15-92  21:46
login.bat         816   9-15-92  21:49
la.com          41361   9-16-92  21:58
alias.lst         275   9-21-92  23:44
autoexec.btm      884   9-24-92  21:10
autoexec.bat       91   9-24-92  21:14
net$dos.sys    535040   9-25-92  15:36
   1,103,847 bytes in 38 file(s)         1,318,912 bytes allocated
 397,205,504 bytes free

[PROGCARE #1-SUPERVISOR]
+F:\LOGIN>map

Drive  A:   maps to a local disk.
Drive  B:   maps to a local disk.
Drive  C:   maps to a local disk.
Drive  D:   maps to a local disk.
Drive  E:   maps to a local disk.
Drive  G: = PROGCARE\SYS:  \LOGIN
      -----
SEARCH1:  = Z:. [PROGCARE\SYS:  \PUBLIC]
SEARCH2:  = Y:. [PROGCARE\SYS:  \BAT]
SEARCH3:  = X:. [PROGCARE\SYS:  \PUBLIC\IBM_PC\MSDOSV5.00]
SEARCH4:  = W:. [PROGCARE\SYS:  \LOGIN]
SEARCH5:  = V:. [PROGCARE\SYS:  \UTILSNET\SABERMU]
SEARCH6:  = U:. [PROGCARE\SYS:  \USAGE]
SEARCH7:  = R:. [PROGCARE\SYS:  \SYSTEM]
SEARCH8:  = T:. [PROGCARE\SYS:  \UTILSWS\PUBLIC]
SEARCH9:  = S:. [PROGCARE\SYS:  \UTILSWS\NORTON]
SEARCH10:  = C:\BAT
SEARCH11:  = C:\DOS
SEARCH12:  = C:\4DOS
SEARCH13:  = C:\MOUSE
SEARCH14:  = C:\UTIL
SEARCH15:  = C:\NETWORK
SEARCH16:  = C:\MULTEDIT
SEARCH17:  = C:\RPGSYS\#SYSTEM
SEARCH18:  = F:\LOGIN [PROGCARE\SYS:  \SYSTEM]
[PROGCARE #1-SUPERVISOR]

                          > > > BOOTFL.BAT < < <

              BOOT IMAGE FILE (NET$DOS.SYS) CREATION ROUTINE
Use this to create or revise anything in the diskless workstation boot image
file.  (For one diskless workstation only!)  See Novell "Installation" manu-
al, Appendix D, pages 349-360.
        1. Make desired revisions to boot image diskette
        2. Run BOOTFL.BAT
        3. Reboot diskless workstation

@echo off
REM BOOTFL.BAT
REM Create diskless workstation boot image file

If not "%1" == "" Call ed a:\%1
If not "%1" == "" if "%1" == "AUTOEXEC.BAT" copy a:\%1 f:\login
If not "%1" == "" if "%1" == "AUTOEXEC.BTM" copy a:\%1 f:\login

map f:=sys:system
map g:=sys:login
g:
DOSGEN
REM Need RPLFIX.EXE patch for DOS5 only.  Get from Netwire.
RPLFIX NET$DOS.SYS

>>>EXECUTE BOOTFL.BAT

+F:\LOGIN>f:

[PROGCARE #1-SUPERVISOR]
+F:\LOGIN>bootfl

Drive F is in use as a search drive.
Do you want to reassign this search drive? (Y/N) Y
Drive  F: = PROGCARE\SYS:  \SYSTEM

Drive  G: = PROGCARE\SYS:  \LOGIN
Floppy Type f9 = Quad Density, 15 Sectors per track
Total Floppy Space 2400 Sectors
Setting Up System Block.
Setting Up FAT Tables.
Setting Up Directory Structures.
Traversing Directory Structures.
Processing IO      SYS
Processing MSDOS   SYS
Diskette Label = DISKLESS WS
Processing COMMAND COM
Processing HIMEM   SYS
Processing BURNDEV SYS
Processing IPX     COM
Processing AUTOEXECBAT
Processing NETX    COM
Processing EMM386  EXE
Processing ANSI    SYS
Processing SHELL   CFG
Processing EMSNETX EXE
Processing 4DOSM   ICO
Processing WAIT    COM
Processing 4DOS    COM
Processing AUTOEXECBTM
Processing 4DOS    PIF
Processing 4DOS    ICO
Processing 4DOS    INI
Processing CONFIG  SYS
Transferring Data to "NET$DOS.SYS"

NetWare Boot Disk Image Patch Program  v1.01 (910226)
(c) Copyright 1991 by Novell, Inc.  All rights reserved.

Boot disk image file has been modified for DOS 5.xx

[PROGCARE #1-SUPERVISOR]
+G:\LOGIN>


>>> Reboot diskless workstation